## Slide 1
Exercises Session on Fault Detection
Giovanni Floreale
giovanni.floreale@polimi.it

## Slide 2
Exercise 1
Component: Gas Turbine

## Slide 3
Exercise 1
Method: PCA
Component: Gas Turbine

## Slide 4: The PCA code in Python: how to run the code?
Import necessary functions and execute the code in one cell:
v=minimum percentage of variance to be represented in the PCA space [e.g., 0.95]
Create a Colab file in your drive in the same folder where data are

## Slide 5: Optimize PCA hyperparameter
Method: PCA
Setting the model parameter:
p = number of principal components
Objective: ACCURATE and ROBUST reconstruction model

## Slide 6: The PCA code in Python: Output
One figure for each signal representing:
The original data and the reconstruction obtained using the PCA algorithm
The residual for each data point
The reconstruction obtained using the PCA algorithm
The number of principal components corresponding to the selected variance
The RMSE

## Slide 7: Accuracy
7
t
t
M
O
D
E
L
INPUT: NORMAL CONDITION DATA
t
t
Signal
reconstructions
Accurate reconstruction model if:
Metric to measure accuracy: Root Mean Square Error ():

## Slide 8: Robustness
8
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:

## Slide 9: Robustness
9
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:
Error to measure Robustness:
Robustness

## Slide 10: Robustness
10
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:
Error to measure Robustness:
Robustness
Normal condition data (before anomaly simulation)

## Slide 11: Robustness
11
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:
Error to measure Robustness:
Robustness
Reconstruction of the anomaly

## Slide 12: Robustness
12
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:
Root mean square Error to measure Robustness:

## Slide 13: Exercise 1.1: Assignment
Consider the same data used in Exercise 1
1. Optimize the PCA reconstruction model to achieve:
  a. Accuracy
  b. Robustness
Hints:
Consider different numbers of Principal Components by trying different values for the parameter v=minimal percentage of variance considered in the PCA space
Consider the root mean square error as a performance measure on test data under normal condition and the robustness metric on test data under simulated abnormal condition
[test_reconstruction,n_PC, RMSE]=PCA_reconstruction(‘train.dat’,’validation.dat’,0.95)
* In python you must first import the function as: from PCA_reconstruction import PCA_reconstruction

## Slide 14: Measured Signals
Temperature location 1 (°C)
Temperature location 2 (°C)
Temperature location 3 (°C)
Temperature location 4 (°C)
Temperature location 5 (°C)
Temperature location 6 (°C)

## Slide 15: Brief Data Description
train.dat  healthy condition data, 6 signals
validation.dat  healthy condition data, 6 signals
val_anomaly.dat  validation data modified with an anomaly on signal 1
validation_sim.dat  validation data modified with an anomaly on signal 6
test_1.dat, test_2.dat, test_3.dat, test_4.dat  test data of unknown health condition

## Slide 16: Exercise 1.2: Assignment
Consider the same data used in Exercise 1
1. Optimize the PCA reconstruction model to achieve:
  a. Accuracy
  b. Robustness
[test_reconstruction,n_PC, RMSE]=PCA_reconstruction(‘train.dat’,’validation.dat’,0.95)
2. Apply the PCA model on test datasets: test_1.dat, test_2.dat, test_3.dat and test_4.dat.

## Slide 17
Sequential Probability Ratio Test (SPRT)

## Slide 18: SPRT: Sequential Probability Ratio Test
COMPARISON
(-)
MODEL OF COMPONENT BEHAVIOR IN NORMAL CONDITIONS (AAKR)
DECISIONSPRT
t
t
t
t
t
MEASURED SIGNALS
t
NORMAL
CONDITION:
No maintenance
ABNORMAL
CONDITION:
maintenance required
…
…
SIGNAL RECONSTRUCTIONS
RESIDUALS

## Slide 19: SPRT: Sequential Probability Ratio Test
How to properly set the residuals thresholds to trigger an alarm?
Sequential Probability Ratio Test

## Slide 20: SPRT: Sequential Probability Ratio Test
0
Assumption: residuals come from two normal distributions with same variance:
Parameters to be set:
the residual variance in normal and abnormal condition (σ)
the expected offset amplitude ()
Our desiderata:
the maximum acceptable false alarm rate (α)
the maximum acceptable missing alarm rate (β)

## Slide 21: SPRT: Sequential Probability Ratio Test
Sequentially compute loglikelihood:
Set decision boundaries:
You are sure you will meet requirements on false and missed alarms ( and )!

## Slide 22: SPRT FUNCTION
OUTPUT:
= -by- vector containing the index
INPUTS:
= -by- data matrix containing N sequential measurements of one signal
= -by-data matrix containing the N reconstructions of the data in .
= Desired false alarm rate
= Desired missed alarm rate.
= the mean of the Gaussian distribution of hypothesis (the component is working in abnormal conditions).
= variance of Gaussian distribution
Example:
save('test_4A_rec_S5.dat', ‘test_reconstruction(:,5)', '-ascii')
Note that the function receives the names of the files containing the data. First you have to save the signal you want to apply SPRT to and then, call it by its name.
Python:
train_data = np.loadtxt(train_data_name); np.savetxt('test_4A_rec_S5.dat',test_reconstruction[:, 4],fmt='%.6f’)
SPRT_Index = SPRT_PCA('test_4B_meas_S5.dat', 'test_4B_rec_S5.dat', alpha, beta, mu1, sigma)

## Slide 23: Exercise 1.3: SPRT
Apply the SPRT to detect abnormal conditions to the measurements of signal 5 in files “test_4A.dat” and “test_4B.dat”. The following setting of the SPRT parameters is suggested:
   trade off among the two + risk of having many points in the “not enough information” region
  Assume Gaussian distributions for the two hypothesis and with parameters:
     could be computed from historical healthy data!
     if no abnormal data are available, we must set these param by assumptions. Hint: residuals will grow as the system gets more abnormal  Offset on the mean and same variance.
Do you detect the occurrence of abnormal conditions? When?
Compare the results with those of a threshold-based method with threshold = 1.
Draw your conclusions on the possibility of using the SPRT in decision-making for fault detection.

## Slide 24: Exercise 1.3: AAKR
Apply the SPRT to detect abnormal conditions to the measurements of signal 5 in files “test_4A.dat” and “test_4B.dat”. The following setting of the SPRT parameters is suggested:
   trade off among the two + risk of having many points in the “not enough information” region
  and Gaussian distributions for the two hypothesis and with parameters:
     can be computed from historical healthy data!
     if no abnormal data are available, we must set these param by assumptions. Hint: residuals will grow as the system gets more abnormal  Offset on the mean and same variance.
Do you detect the occurrence of abnormal conditions? When?
Compare the results with those of a threshold-based method with threshold = 1.
Draw your conclusions on the possibility of using the SPRT in decision-making for fault detection.

## Slide 25
Exercise 2
Method: you choose
Component: Wind Turbine

## Slide 26: The Monitoring System
  Main Bearing+ Planetary Gear box + Gearbox + Generator
  Monitoring system: 6 accelerometers and 1 sensor measuring the rotating speed.
Wind turbine farm

## Slide 27: Some possible failures modes
  Crashing of the highspeed shaft of the gear box
  Breaking of a teeth in the planetary stage
  Misalignment between the generator and the gearbox shafts
  Wearing of the rear bearing housing of the generator

## Slide 28: Example
Wearing of the rear bearing housing of the generator
Vibration feature
Maintenance intervention

## Slide 29: Corrective Maintenance
Gearbox-Generator Failure
    Long turbine downtime [up to some months]
    Intervention of expensive tools

## Slide 30: Feature Extraction
…
Window 1
Features
Window 2
Features
Window 3
Features
High frequency sensor:
10 k observations
10 k observations
10 k observations

## Slide 31: Feature Extraction
…
Window 1
Window 2
Window 3
Feature 1
Time t
Feature 2
Time t
…

## Slide 32: Feature Extraction
…
Window 1
Window 2
Window 3
Feature 1
Time t
Feature 2
Time t
Fault Detection
Normal
Abnormal

## Slide 33: FEATURE EXTRACTION
Sample Mean:
Sample Variance:
Standard Deviation:
-th Moments:
Kurtosis  “peak”
(the fourth standardized moment)
Skewness “asymmetry” (the third standardized moment)
Each 5 sec signal data are divided in 40 segments(windows) in order to extract features
The following statistical features are considered:
Mean, standard deviation, Kurtosis, Skewnesss, min, max, 2nd moment, 3rd moment
A window contains values , the corresponding Statistical Features are:

## Slide 34: FEATURE EXTRACTION
0
5

## Slide 35: Exercise 2: Assignment
Col 1 | Col 2 | Col 3 | Col 4 | Col 5 | Col 6 | Col 7 | Col 8
mean | std | kurtosiss | skewness | min | max | 2nd Moment | 3rd Moment
In folder Exercise 2 you find:
  The file ‘train.dat’ which contains the features already extracted in normal condition
  The file ‘validation.dat’ which contains the features already extracted in normal condition
  The file ‘validation_sim.dat’ which contains a simulated abnormal condition on signal 3
  The files for testing ‘test1.dat’ and ‘test2.dat’
  Each of these files contains the following signals:
You are required to:
  Develop and optimize a fault detection tool for the turbine generator;
  Apply the developed tool to the data in the files test1 and test2 to identify possible abnormal conditions period.